Soils Layers and Depth Analysis
These happen from beginning of simulation to end in order. Anything later will potentially replace earlier items.

The default Soil Layer Structure is from SoilLayers. Problem?: If (no treatment soilsin and no data in soils datafile) we will could have a mismatch between the default swRun soils default and SoilLayers datafile.)

1.) SoilsLayers Datafile
a.) sets SoilDepth and the depth of each layer

2.) ExtractSoilDataFromCONUSSOILFromSTATSGO_NorthAmerica
a.) replaces soil structure in SoilsLayers Datafile and sets use column

DoOneSite

i_sw_input_soillayers <- sw_input_soillayers #for one site

3.)	a. soilsin set in treatments or experimentals
1. Grab data from tr_soil file and set
2. layers_depth, d and soildepth
3. Replace swRunScenarioData Soil data with tr_soil
b. soilsin not set in treatments or experimentals
1. soildepth <- i_sw_input_soillayers # soildepth_cm column
2. layers_depth <- i_sw_input_soillayers # depth_L columns that are filled in
3. d <- smallest layer that has depth equal to or greater then soildepth
c.) adjust layers_depth to whole number for d layers
d.) layers_width is calculated from layers_depth
e.) Calc DeepestTopLayer, topL, bottomL from above data and user input, Depth_TopLayers.

4.) if sw_input_soils_use has columns besides transpregion set
Compare SoilLayers and swRunScenarioData Soils soil depth and layers info
1. Identical
Layer structure does not change
2. !Identical
a. Recalc d, layer_depth, layer_width, ld, DeepestTopLayer, topL, bottomL based on soils datafile
Adjust deepest soil layer if there is no soil information for the lowest layers, but needs to recalculate soil layer structure
1. Find deepest layer where bulkd, sand, clay all have data, not na and > 0.
a. if that layer is not the same as d readjust d, layer_depth, layer_width, ld, DeepestTopLayer, topL, bottomL to that layer.

Evaporation Coefficient Source
These happen from beginning of simulation to end in order. Anything later will potentially replace earlier items.

Before doOne Site

1. Soils Input Data File
a.) header columns for EvapCoeff is set to one

2. treatments LookupEvapCoeffFromTable and not experiments LookupEvapCoeffFromTable
a.) treatments “LookupEvapCoeffFromTable” set No NAs in column
b.) trfile.LookupEvapCoeffFromTable file set
c.) Replaces sw_input_soils and sets sw_input_soils_use
d.) Writes sw_input_soils to file

3. exinfo$CalculateBareSoilEvaporationCoefficientsFromSoilTexture
a.) Need 1 or more Sand_L in sw_input_soils
b.) Replaces sw_input_soils and sets sw_input_soils_use

In doOne Site

4. treatments LookupEvapCoeffFromTable
a.) expirements “LookupEvapCoeffFromTable” set No NAs in column
b.) trfile.LookupEvapCoeffFromTable file set
c.) Replaces i_sw_input_soils and sw_input_soils_use <- i_sw_input_soils is a single row from sw_input_soils given to the run.

5.) Merge of soils.in file and i_sw_inpu_soils only done if flags are set in soils datafile. Flags are changed in all of the above steps
a.) if soils.in and i_sw_input_soils depths are identical
1.) Use defualt values of soils.in replace with data set in i_sw_input_soils
b.) if different soil depth from i_sw_input_soils and soils.in
1.) Everything is based off of i_sw_input
2.) evco, trco_grass, trco_shub, trco_tree, imperm: default to 0 if missing
3.) Drop layer if no i_sw_input_soils data for bulkd, sand, clay
3.) bulk fielddc wiltp sand clay: use previous layer value if missing

TRCO Coefficient Source
These happen from beginning of simulation to end in order. Anything later will potentially replace earlier items.

1. Soils Input Data File
a.) header columns for trco_grass, trco_shrub, trco_tree Coeff is set to one

In doOne Site

2.) treatment's or experimental's LookupTranspCoeffFromTable_Grass, LookupTranspCoeffFromTable_Shrub, LookupTranspCoeffFromTable_Tree set
a.) data is read in from treatments trco table
b.) i_sw_input_soils data is replaced/written with new values
c.) sw_input_soils_use set

3.) Merge of soils.in file and i_sw_inpu_soils only done if any flags are set in soils datafile but not regions flag. Flags are changed in all of the above steps
a.) if soils.in and i_sw_input_soils depths are identical
1.) Use defualt values of soils.in replace with data set in i_sw_input_soils
b.) if different soil depth from i_sw_input_soils and soils.in
1.) Everything is based off of i_sw_input
2.) evco, trco_grass, trco_shub, trco_tree, imperm: default to 0 if missing
3.) Drop layer if no i_sw_input_soils data for bulkd, sand, clay
3.) bulk fielddc wiltp sand clay: use previous layer value if missing

4.) Adjust Root profile
a.) PotentialNaturalVegetation_CompositionShrubsC3C4_Paruelo1996 has to be set in treatments or experimental
b.) Root profile in treatments or experimental have to match tr_input_TranspCoeff column names.
c.) new trco values are used.